## Slide 1
Handled by
S. Murali, Ph.D.,
Associate Professor,
Department of Mechanical Engineering, SRM IST, Kattankulathur.
Subject Code
18MEO113T - Design of Experiments
Disclaimer
The content prepared in the presentation are from various sources, only used for education purpose. Thanks to all the sources.

## Slide 2
Unit 4

## Slide 3: Unit 4

## Slide 4: Assumptions of Linearity in two-level designs
In general, significant proportion of experiments are performed with two-level factorials.
Two-level full factorial designs with k factors are denoted as 2k
These models assume linear response
For example, linear regression model of 22 design is:
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 5: Assumptions of Linearity in two-level designs
Two-level factorial designs assumes linearity of response
In reality, the response may not be linear
The more the curvature or non-linearity, the more will be error in the prediction of interim values.
0
+1
-1
y
If the linearity is not large, the error in predicting interim values predicted by the model can be large.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 6: Assumptions of Linearity in two-level designs
How to minimize effect of non-linearlity
One possible recommendation is to select levels of the factors as close as possible.
This will help reducing the error. However, it will affect the magnitude of the effect/ response.
0
+1
-1
y
Magnitude of effect will be reduced.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 7: Addition of Center Point
Therefore experimenters often add a center point in the design.
The purpose of adding a center point is to validate the assumption of linearity.
If the response at the center point is significantly different than the predicted value on the straight line, then a non linear model will be required to reduce the error. This can be done with a Response Surface Design.
0
+1
-1
22 design with center point
A
+1
-1
B
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 8: Background of response surface design
Response Surface Methodology, or RSM, is a collection of mathematical and statistical techniques useful for the modeling and analysis of problems in which a response of interest is influenced by several variables and the objective is to optimize this response.
Response (Ex: Process yield, defects, etc.)
Zi
Xi
Process/System
Setting the X in the particular range or zone by that we can able to get the optimal response value.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 9: Background of response surface design
RSM, is a collection of mathematical and statistical techniques useful for the developing, improving, and optimizing processes.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 10: Background of response surface design
The difference between a response surface equation and the equation for a factorial design is the addition of the squared (or quadratic) terms that lets you model curvature in the response, making them useful for:
  Understanding or mapping a region of a response surface. Response surface equations model how changes in variables affect a response of interest.
  Finding the levels of variables that optimize a response.
  Selecting the operating conditions to meet specifications.
For example, you would like to determine the best conditions for injection-molding a plastic part. You first used a screening or factorial experiment to determine the significant factors (temperature, pressure, cooling rate). You can use a response surface designed experiment to determine the optimal settings for each factor.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 11: Background of response surface design
The difference between a response surface equation and the equation for a factorial design
A two-level factorial (or fractional factorial) design looks for linear trends, possibly with interactions
  Does the variable significantly impact the response? In what direction?
  It helps to define the next experiment.
Response Surface Methodology (RSM) looks for quadratic or higher order trends
  Assumes all variable are significant
  A quadratic response always has a stationary point (minimum or maximum or saddle point)
  Can be used to optimize a process
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 12: Background of response surface design
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 13: Background of response surface design
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 14: Background of response surface design
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 15: Background of response surface design
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 16: Background of response surface design
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 17: Background of response surface design
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 18: Background of response surface design
The Method of Steepest Ascent
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 19: Example 1 (First-order RSM)
A chemical engineer is interested in determining the operating conditions that maximize the yield of a process. Two controllable variables influence process yield: reaction time and reaction temperature. The engineer is currently operating the process with a reaction time of 35 minutes and a temperature of 155°F, which result in yields of around 40 percent. Because it is unlikely that this region contains the optimum, she fits a first-order model and applies the method of steepest ascent.

## Slide 20: Example 1 (RSM First-order Model)
Response variable = Process yield = Y = 40%
Current operating condition:
  Natural variable ) = Coded variable (X1) = Reaction time of 35 minutes
  Natural variable ) = Coded variable (X2) = Temperature of 155°F
X1
X2
40
30
150
160
Temp
Time
(35, 155)
2K factorial design with center point
X1: High = 40 min (+1); Low = 30 min (-1)
X2: High = 160 F (+1); Low = 150 F (-1)

## Slide 21: Example 1 (First-order RSM)
40.44 = Average of all Y observation ()…
= = 0.775
= = 0.325
Y=++

## Slide 22: Example 1 (First-order RSM)
In order to check, whether the first-order model fitted or not, we have to check the following:
  Estimate the Error (based on central point observation)
  Test for Interaction ( whether significant or not?
  Test for Quadratic effects ( whether significant or not?
  If step 2 and step 3 is equal to zero, then we can say the first-order model is fit. If not, we have to analysis further.

## Slide 23: Example 1 (First-order RSM)
Step 1. Estimate the Error (based on central point observation)
Error = [Sum of square of all the values/responses – (squares of sum of all the values)/n] / n-1
The mean square Error (MSE) = 0.0430

## Slide 24: Example 1 (First-order RSM)
Step 2. Test for Interaction Estimate the Error
The first-order model assumes that the variables x1 and x2 have an additive effect on the response. The interaction between the variables would be represented by the coefficient of of a cross-product term x1x2 added to the model.
The least squares estimate of this coefficient is just one-half the interaction effect calculated as in an ordinary 22 factorial design,

## Slide 25: Example 1 (First-order RSM)
Step 2. Test for Interaction Estimate the Error
Test for Interaction ( whether significant or not?
So, Hypothesis H0 = = 0
Alternative H1 = ≠ 0
can be estimated from factorial points.
So Interaction = Average of (39.3+41.5) – Average of (40+40.9)] = - 0.025
(or)
AB = 41.5+39.3-40.9-40]
Hence, Interaction = AB/2 = 41.5+39.3-40.9-40] = -0.025
40.9
39.3
41.5
40

## Slide 26: Example 1 (First-order RSM)
Step 2. Test for Interaction Estimate the Error
Test for Interaction ( whether significant or not?
Hence, Interaction = -0.025 with DOF = 1
MSE = 0.0430 with DOF = 4
We have to know whether interaction is significant or not, hence, compare the interaction value with MSE
F = …which is small and insignificant or negligible.

## Slide 27: Example 1 (First-order RSM)
Step 3: Test for Quadratic effects whether significant or not?
whether
= 40.425 – 40.46 = -0.035
Hypothesis H0 = = 0
Alternative H1 =≠ 0
…which is small, hence, there is no indication of a pure quadratic effect.
Factorial portion
Factorial portion
Factorial portion
Factorial portion
Center point
So, quadratic effect not there…interaction effect not there…hence, the first-order model is fit one.

## Slide 28: Example 1 (First-order RSM)
0.02953
SS Total =(39.32+ 402+ 40.92+ 41.52+ 40.32+ 40.52+ 40.72+ 40.22+ 40.62) – [(39.3+40+40.9+41.5+40.3+40.5+40.7+40.2+40.6)2/9] =3.0022
SS Model = SS total – SS residual = 3.0022 – 0.1772 = 2.8250
F-Model = 2.8250/0.02953 = 47.83

## Slide 29: Example 1 (First-order RSM)
Hence, we can say is fit one…..
However, we need to ensure whether the parameters and is significant….by doing Test of Parameter Estimates..
For that, we need to identify the variance of ….i.e., V()
V() =
SE() = =
Both regression coefficients and are large relative to their standard errors. At this point, we have no reason to question the adequacy of the first-order model.

## Slide 30: Example 1 (First-order RSM)
X1 (Time)
X2 (Temp)
Center point (0,0)

## Slide 31: Example 1 (First-order RSM)
40
35, 155
85, 175
30
160
150
90
80
180
170

## Slide 32: Example 1 (First-order RSM)
78.97 = Average of all Y observation ()…
= = 1
= = 0.5

## Slide 33: Example 1 (First-order RSM)

## Slide 34: Analysis of a Second-Order Response Surface

## Slide 35: Analysis of a Second-Order Response Surface

## Slide 36: Analysis of a Second-Order Response Surface

## Slide 37: Analysis of a Second-Order Response Surface

## Slide 38: Analysis of a Second-Order Response Surface

## Slide 39: Analysis of a Second-Order Response Surface

## Slide 40: Example for Second-Order Response Surface.
Response surface for certain manufacturing process was defined by the given equation(). Determine the approximate optimum operating point using the method of steepest ascent. The starting point of research should be X1=2 and X2=3 and step size C=4.
Step size = 4.0
=

## Slide 41: Example.
Hence,
New, x1 and x2..i.e.,
=
=

## Slide 42: Example.
= 188.981
New, x1 and x2..i.e.,
=
=
= 245.3

## Slide 43: Example.
= 245.3
New, x1 and x2..i.e.,
=
=
= 272.19

## Slide 44: Example.
= 272.19
New, x1 and x2..i.e.,
=
=
= 269.84

## Slide 45: Example.
Current operating condition
Contours of constant response
Optimum region

## Slide 46: Features for selecting response surface design

## Slide 47: Design for fitting the Second-Order Model
There are two main types of response surface designs:
Central Composite designs (CCD)
  Central Composite designs can fit a full quadratic model. They are often used when the design plan calls for sequential experimentation because these designs can include information from a correctly planned factorial experiment.
Box-Behnken designs (BBD)
  Box-Behnken designs usually have fewer design points than central composite designs, thus, they are less expensive to run with the same number of factors. They can efficiently estimate the first- and second-order coefficients; however, they can't include runs from a factorial experiment. Box-Behnken designs always have 3 levels per factor, unlike central composite designs which can have up to 5. Also unlike central composite designs, Box-Behnken designs never include runs where all factors are at their extreme setting, such as all of the low settings.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 48: Central Composite designs (CCD)
Central Composite designs (CCD)
A central composite design is the most commonly used response surface designed experiment. Central composite designs are a factorial or fractional factorial design with center points, augmented with a group of axial points (also called star points) that let you estimate curvature. You can use a central composite design to:
  Efficiently estimate first- and second-order terms.
  Model a response variable with curvature by adding center and axial points to a previously-done factorial design.
Central composite designs are especially useful in sequential experiments because you can often build on previous factorial experiments by adding axial and center points.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 49: Central Composite designs (CCD)
Central Composite designs (CCD)
For example, you would like to determine the best conditions for injection-molding a plastic part. You first run a factorial experiment and determine the significant factors: temperature (levels set at 190° and 210°) and pressure (levels set at 50MPa and 100MPa). If the factorial design detects curvature, you can use a response surface designed experiment to determine the optimal settings for each factor.
Notes: https://www.youtube.com/watch?v=O0NF4tKe5lM&t=3s

## Slide 50: Central Composite designs (CCD)
Central Composite designs (CCD)..continued
Notes: https://support.minitab.com/en-us/minitab/18/help-and-how-to/modeling-statistics/doe/supporting-topics/response-surface-designs/response-surface-central-composite-and-box-behnken-designs/

## Slide 51: Central Composite designs (CCD)
Three parts:
1.
Factorial or reduced factorial design Estimate of main effects and interactions
2.
At least one center point experiment Possible to reveal curvature and estimate the experimental error
3.
Experiments  on the variable axes Possible to estimate quadratic terms

## Slide 52: Central Composite designs (CCD)
Central Composite Design (CCD) has three different design points: edge points as in two‐ level designs (±1), star points at ±α; ׀α׀ ׀≤1 that take care of quadratic effects and centre points,
Three variants exist:
Circumscribed (CCC)
Face centered (CCF)
Inscribed (CCI)

## Slide 53: Central Composite designs (CCD)
nf = The number of factorial run

## Slide 54: Central Composite designs (CCD)

## Slide 55: Central composite rotatable design for two variables
Number of experiments: 23 + 4 + 6 = 18

## Slide 56: Central composite rotatable design for three variables

## Slide 57: Central Composite designs (CCD)

## Slide 58: Central Composite designs (CCD)
Number of runs required for CCD and its types, and 3k design

## Slide 59: Box-Behnken designs (BBD)
Box-Behnken designs (BBD)
Box-Behnken designs have treatment combinations that are at the midpoints of the edges of the experimental space and require at least three continuous factors. The following figure shows a three-factor Box-Behnken design. Points on the diagram represent the experimental runs that are done:
Notes: https://support.minitab.com/en-us/minitab/18/help-and-how-to/modeling-statistics/doe/supporting-topics/response-surface-designs/response-surface-central-composite-and-box-behnken-designs/

## Slide 60: Box-Behnken designs (BBD)
Box-Behnken designs (BBD)
A Box-Behnken design is a type of response surface design that does not contain an embedded factorial or fractional factorial design.
For example, you would like to determine the best conditions for injection-molding a plastic part. The factors you can set are:
  Temperature: 190° and 210°
  Pressure: 50Mpa and 100Mpa
  Injection speed: 10 mm/s and 50 mm/s
For a Box-Behnken design, the design points fall at combinations of the high and low factor levels and their midpoints:
  Temperature: 190°, 200°, and 210°
  Pressure: 50Mpa, 75Mpa, and 100Mpa
  Injection speed: 10 mm/s, 30 mm/s, and 50 mm/s
Notes: https://support.minitab.com/en-us/minitab/18/help-and-how-to/modeling-statistics/doe/supporting-topics/response-surface-designs/response-surface-central-composite-and-box-behnken-designs/

## Slide 61: Box-Behnken designs (BBD)

## Slide 62: Box-Behnken designs (BBD)

## Slide 63: Box-Behnken designs (BBD)

## Slide 64: Box-Behnken designs (BBD)

## Slide 65
Thank you